## Slide 1: MIPS Assembly Language
Category
Arithmetic
Data Transfer
Conditional branch
Instruction
add
subtract
Example
add $1,$2,$3
sub $1,$2,$3
Meaning
$1 = $2 + $3
$1 = $2 - $3
load word
store word
branch on equal
branch on not equal
lw $1,100($2)
sw $1,100($2)
beq $1,$2,L
bne $1,$2,L
$1=m[$2+100]
m[$2+100]=$1
if($1==$2) goto L
if($1!=$2) goto L
UnconditionalJump
jump
jump register
j 10000
jr $31
go to 10000
go to m[$31]

## Slide 2: MIPS Machine Language
Name
Format
Field Size
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
Example
Comments
R-format
R
op
rs
rt
rd
shamt
funct
Arithmetic
I-format
I
op
rs
rt
address
Data transfer
add
R
0
18
19
17
0
32
add $17, $18, $19
sub
R
0
18
19
17
0
34
sub $17, $18, $19
lw
I
35
18
17
100
lw $17, 100($18)
sw
I
43
18
17
100
sw $17, 100($18)

## Slide 3: Field Definitions
op: Instruction opcode
rs: The 1st register source operand.
rt: The 2nd register source operand.
rd: The destination register.
Ssamt: Shift amount.
funct: Function code.

## Slide 4: lw instruction
e.g., lw $t0, 1200($t1)
lw $8, 1200 ($9)
The base register 9 ($t1) is specified in the second field (rs),
The destination register 8 ($t0) is specified in the third field (rt)

## Slide 5: lw
In a load word instruction the meaning of the rt field specifies the destination register, which receives the result of the load.

## Slide 6: I-format Instructions
Name
Format
Field Size
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
Example
Comments
I-format
I
op
rs
rt
address
Data transfer
addi
I
8
2
1
100
addi $1, $2, 100
beq
I
4
1
2
25
beq $1, $2, 25
bne
I
5
1
2
25
bne $1, $2, 25
slti
I
10
2
1
100
slti $1, $2, 100